## Slide 1: About the Presentations
The presentations cover the objectives found in the opening of each chapter.
All chapter objectives are listed in the beginning of each presentation.
You may customize the presentations to fit your class needs.
Some figures from the chapters are included. A complete set of images from the book can be found on the Instructor Resources disc.

## Slide 2: A+ Guide to Managing and Maintaining Your PC, 7e
Chapter 1
Introducing Hardware

## Slide 3: Objectives
A+ Guide to Managing and Maintaining Your PC, 7e
Learn that a computer requires both hardware and software to work
Learn about the many different hardware components inside of and connected to a computer

## Slide 4: Hardware Needs Software to Work
A+ Guide to Managing and Maintaining Your PC, 7e
Hardware
  Computer’s physical components
    Monitor, keyboard, memory, hard drive
Software
  Instruction set
    Directs hardware to accomplish a task
  Uses hardware for four basic functions
    Input, processing, storage, output
Hardware components
  Require an electrical system

## Slide 5
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-1 Computer activity consists of input, processing, storage, and output
Courtesy: Course Technology/Cengage Learning

## Slide 6: Hardware Needs Software to Work (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
User interaction with computer
  User and software communicate with input device
  Hardware uses two states: on and off
Figure 1-2 All communication, storage, and processing of data inside a computer are in binary form until presented as output to the user
Courtesy: Course Technology/Cengage Learning

## Slide 7: Hardware Needs Software to Work (cont’d.)
Binary number system
  Stores and reads two states
    Zero or one
  Bit: binary digit
    Value of zero or one
  Nibble: four bits
  Byte: eight bits
  Used for counting, calculation, storage operations
American Standard Code for Information Interchange (ASCII)
  Used for storing information
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 8
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-3 All letters and numbers are stored in a computer as a series of bits, each represented in the computer as on or off
Courtesy: Course Technology/Cengage Learning

## Slide 9: Hardware Needs Software to Work (cont’d.)
Hexadecimal number system
  Base 16 number system
  Counts from 0 to F, where A=10, B=11, C=12, D=13, E=14, F=15
  Used in many aspects in computing like, Memory Addresses, Color System for Web, IPv6 addressing for Networking
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 10: Hardware Needs Software to Work (cont’d.)
Hexadecimal number system
  6510 is not the same as 6516
  6510 is 4116
  41 is 4 (x161) + 1 (x160)
  64 + 1 = 6510
Convert the following decimal numbers to Hexadecimal
24010
64010
97210
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 11: Activity 1
Set A or Set B
  What are the ASCII Equivalents of the 1st five letters of your first name or last name?
Set A
  Convert the following:
    247 to Binary
    247 to Hexadecimal
Set B
  Convert the following
    252 to Binary
    252 to Hexadecimal
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 12: PC Hardware Components
A+ Guide to Managing and Maintaining Your PC, 7e
Input/output (I/O) devices: external to the case
Processing, storage devices: internal to the case
Central processing unit (CPU)
  Also called: processor, microprocessor
  Reads input, processes data, writes data to storage
Elements required by I/O, storage devices
  Method for CPU to communicate with the device
  Software to instruct, control the device
  Electricity to power the device

## Slide 13: Hardware Used for Input and Output
A+ Guide to Managing and Maintaining Your PC, 7e
I/O device communication with computer components
  Wireless
  Cabled using a port
    Access point located in back or front of case
Primary input devices
  Keyboard, mouse
    Requires electricity from inside case
Primary output devices
  Monitor: visually displays primary computer output
  Printer: produces paper output (hard copy)

## Slide 14
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-4 Input/output devices connect to the computer case by ports usually found on the back of the case
Courtesy: Course Technology/Cengage Learning

## Slide 15: Lab Exercise
    Page 31 (Project 1-1)
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 16
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-5 The keyboard and the mouse are the two most popular input devices
Courtesy: Course Technology/Cengage Learning
Figure 1-6 The two most popular output devices are the monitor and the printer
Courtesy: Course Technology/Cengage Learning

## Slide 17
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-7 Two video connectors and two connectors used by a printer
Courtesy: Course Technology/Cengage Learning

## Slide 18: Hardware Inside the Computer Case
Storage and processing occurs in the case
Internal devices common to most computers
  Motherboard containing CPU, memory, other parts
  Hard drive, optical drive for permanent storage
  Power supply with power cords supplying electricity
  Adapter cards for internal and external communication
  Cables to connect devices
Adapter card installed in expansion slots
Cable types
  Data (communication) and power
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 19
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-8 Inside the computer case
Courtesy: Course Technology/Cengage Learning

## Slide 20: The Motherboard
A+ Guide to Managing and Maintaining Your PC, 7e
Largest, most important circuit board
  Main board or system board
  Contains the CPU, expansion slots, other devices
Motherboard component categories
  Processing, temporary storage, communication, power
All devices communicate with motherboard CPU
Peripheral device links to motherboard via cable
Motherboard ports may be outside of the case
  Keyboard, mouse, parallel, USB ports, sound ports

## Slide 21
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-9 All hardware components are either located on the motherboard or directly or indirectly connected to it because they must all communicate with the CPU
Courtesy: Course Technology/Cengage Learning

## Slide 22
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-10 A motherboard provides ports for common I/O devices
Courtesy: Course Technology/Cengage Learning

## Slide 23: The Processor and the Chipset
CPU
  Chip inside the computer
  Performs most data processing
Chipset
  Group of microchips controlling data flow
Personal computer (PC)
  Focus of this text
Major CPU, chipsets manufacturers
  Intel Corporation, AMD
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 24
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-11 The processor is hidden underneath the fan and the heat sink, which keep it cool
Courtesy: Course Technology/Cengage Learning

## Slide 25: Storage Devices
A+ Guide to Managing and Maintaining Your PC, 7e
Primary storage (main memory)
  Temporary storage used by the processor
Secondary storage (permanent storage)
  Enables data to persist after machine turned off
  Examples: hard drive, CD, DVD, USB drive
Primary-secondary memory relationship analogy
  Library book stacks: permanent storage
  Books moved to a desk: temporary storage

## Slide 26
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-12 Memory is a temporary place to hold instructions and data while the CPU processes both
Courtesy: Course Technology/Cengage Learning

## Slide 27: Primary Storage
A+ Guide to Managing and Maintaining Your PC, 7e
Provided by random access memory (RAM)
  Located on motherboard, adapter cards
RAM chips
  Embedded on small board
  Plugs into motherboard
  Most common: dual inline memory module (DIMM)
  Video memory: embedded on video card
Volatile memory
Non-volatile memory

## Slide 28
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-13 A DIMM holds RAM and is mounted directly on a motherboard
Courtesy: Course Technology/Cengage Learning

## Slide 29: Secondary Storage
A+ Guide to Managing and Maintaining Your PC, 7e
Remote storage locations containing data and instructions
  Cannot be directly processed by CPU
  Permanent
Hard drives
  Main secondary computer storage device
  Magnetic hard drives
    Use Integrated Drive Electronics (IDE)
  Solid state drive (SSD)
    Use nonvolatile flash memory

## Slide 30
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-15 Hard drive with sealed
cover removed
Courtesy: Seagate Technologies LLC
Figure 1-16 Four SSD drives
Courtesy: Course Technology/Cengage Learning

## Slide 31: Secondary Storage (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
Hard drives (cont’d.)
  ATA (AT Attachment) standard
    Specifies motherboard-hard drive interface
    Types: serial ATA (SATA), parallel ATA (PATA)
  Serial ATA standard
    External SATA (eSATA)
    Usually two to eight SATA and eSATA connectors
  Parallel ATA (PATA)
    Slower than SATA
    Two connectors on a motherboard for two data cables
    Accommodates up to four IDE devices

## Slide 32
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-18 Using a parallel ATA interface, a motherboard has two IDE connectors, each of which can accommodate two devices; a hard drive usually connects to the motherboard using the primary IDE connector
Courtesy: Course Technology/Cengage Learning

## Slide 33
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-19 Two IDE devices connected to a motherboard using both IDE connections and two cables
Courtesy: Course Technology/Cengage Learning

## Slide 34
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-20 This system has a CD-ROM and a Zip drive sharing
the secondary IDE cable and a hard drive using the primary IDE cable
Courtesy: Course Technology/Cengage Learning

## Slide 35: Secondary Storage (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
Optical drives
  RW can write to a disk
  ROM (read-only memory) can only read a disc
Figure 1-22 This CD drive is an EIDE device and connects to the motherboard by way of an IDE data cable
Courtesy: Course Technology/Cengage Learning

## Slide 36: Secondary Storage (cont’d.)
USB flash drives and memory cards
  Popular, nonvolatile flash memory chips
  Compact; easy to use; currently hold up to 64 GB of data
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-24 Most laptops have a memory card slot that can accommodate an SD card
Courtesy: Course Technology/Cengage Learning

## Slide 37: Secondary Storage (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
Floppy drive
  Older secondary storage device
  3.5-inch disk holding 1.44 MB of data
  Floppy drive connector
    Distinct from IDE connectors
    Floppy drive cable accommodates one or two drives

## Slide 38: Activity 2
Go to the Internet research on the topics shown below and write a small essay in paragraph form and in your own words citing the main difference between the two technologies.
  HDD vs SSD
  PATA vs SATA
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 39: Motherboard Components Used For Communication Among Devices
A+ Guide to Managing and Maintaining Your PC, 7e
Traces
  Fine lines on top and bottom of the motherboard’s surface
Bus
  System of pathways, transmission protocols
Data bus
  Carries the data

## Slide 40
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-27 On the bottom of the motherboard, you can
see bus lines terminating at the CPU socket
Courtesy: Course Technology/Cengage Learning

## Slide 41: Motherboard Components Used For Communication Among Devices (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
Binary data corresponds to voltage on the line
  Voltage, lack of voltage interpreted as binary digits
Data bus sizes today
  16, 32, 64, 128, 256 bits wide
  Some use error checking bit
Figure 1-28 A data bus has traces or lines that carry voltage interpreted by the CPU and other devices as bits Courtesy: Course Technology/Cengage Learning

## Slide 42: Motherboard Components Used For Communication Among Devices (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
Data path size
  Width of a data bus
Motherboard can have more than one bus
  Main motherboard bus
    Communicates with CPU, memory, chipset
    Also called system bus, front side bus (FSB), memory bus, host bus, local bus, external bus
System clock
  Dedicated to timing motherboard chip activities
  Quartz crystal generates oscillation

## Slide 43
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-29 The system clock is a pulsating electrical signal sent out by this component that works much like a crystal in a wristwatch (one line, or circuit, on the motherboard bus is dedicated to carrying this pulse)
Courtesy: Course Technology/Cengage Learning

## Slide 44: Motherboard Components Used For Communication Among Devices (cont’d.)
Devices work according to beats (or cycles)
Clock speed measured in hertz (cycles/second)
  One megahertz (MHz): one million cycles per second
  One gigahertz (GHz): one billion cycles per second
Common ratings for motherboard buses
  2600 MHz, 2000 MHz, 1600 MHz, 1333 MHz, 1066 MHz, 800 MHz, 533 MHz, or 400 MHz
Range of CPU speeds: 166 MHz to 4 GHz
Buses for expansion slots: PCI, AGP, ISA
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 45
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-30 The lines of a bus terminate at an expansion slot where they connect to pins that connect to lines on the expansion card inserted in the slot
Courtesy: Course Technology/Cengage Learning

## Slide 46
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-31 The one AGP slot used for a video card is set farther from the edge of the board than the PCI slots
Courtesy: Course Technology/Cengage Learning

## Slide 47: Expansion Cards
A+ Guide to Managing and Maintaining Your PC, 7e
Some names for circuits mounted in expansion slots
  Circuit cards, adapter boards, expansion cards, cards
Cards that connect the CPU to an external device
  Video: provides a port for the monitor
  Sound: provides ports for speakers and microphones
  Network: provides a port for a network cable
  Modem: provides ports for phone lines
Determine a card’s function by identifying its port

## Slide 48
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-32 This adapter card is a modem card and is
mounted in a PCI slot on the motherboard
Courtesy: Course Technology/Cengage Learning

## Slide 49
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-34 The easiest way to identify this video card is to look at the ports on the end of the card
Courtesy: Course Technology/Cengage Learning

## Slide 50: The Electrical System
A+ Guide to Managing and Maintaining Your PC, 7e
Power supply
  Most important electrical component
  Converts AC voltage external source to DC voltage
  Reduces voltage from 110-120 volts to 12 volts or less
  Runs a fan to cool the inside of the computer case
Temperatures > 185° F can cause component failure
Motherboard has 1 or 2 connections to power supply

## Slide 51
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-36 The motherboard receives its power from the power supply by way of a 20 or 24-pin connector called the P1 connector
Courtesy: Course Technology/Cengage Learning

## Slide 52: Instructions Stored on the Motherboard and Other Boards
BIOS (basic input/output system)
  Data and instructions stored on ROM chips
  ROM BIOS chips: type of firmware
Three purposes served by motherboard ROM BIOS
  System BIOS: manages simple devices
  Startup BIOS: starts the computer
  CMOS setup: changes motherboard settings
CMOS RAM: includes date, time, port configurations
Flash ROM
  ROM chips that can be overwritten
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 53
A+ Guide to Managing and Maintaining Your PC, 7e
Figure 1-37 This firmware chip contains flash ROM and CMOS RAM; CMOS RAM is powered by the coin battery located near the chip
Courtesy: Course Technology/Cengage Learning

## Slide 54: Activity 3
Set A
  Answer all the even numbered Questions on Review the Basics from Pages 29-30
Set B
  Answer all the odd numbered Questions on Review the Basics from Pages 29-30
A+ Guide to Managing and Maintaining Your PC, 7e

## Slide 55: Summary
A+ Guide to Managing and Maintaining Your PC, 7e
A computer comprises hardware and software
Main functions
  Input, output, processing, storage
Data stored in a binary format (one or zero, on or off)
Input/output devices
  Keyboard, mouse, printer, monitor
Motherboard (system board)
  Contains CPU, access to other circuit boards, peripherals

## Slide 56: Summary (cont’d.)
A+ Guide to Managing and Maintaining Your PC, 7e
Primary storage (RAM): volatile
Secondary storage: nonvolatile
Parallel and serial ATA standards
  Enable secondary storage devices to interface with the motherboard
Computer bus
  System of communication pathways, protocols
ROM BIOS
  Helps start PCs; manages simple devices; changes some motherboard settings